## Slide 1: Seasonal energy storage for the circular economy of the future with high energy density
Holger Ihssen
Helmholtz / KIT
Brussels Helmholtz Office
Items of today
European Energy Research
2050 Storage Demand
Aluminium as Storage Medium
Storage System Costs
StoRIES Project

## Slide 2: European Energy Research
1

## Slide 3: Policy and Energy Storage
Circular economy
Society
Per-and Polyfluoroalkyl Substances (PFAS)
Energy Storage
System Scale Up

## Slide 4: European Energy Research Alliance (EERA)
EERA in a nutshell: The European Energy Research Alliance is a membership-based, non-profit association, constituting the largest low-carbon energy research community in Europe and a key player in the European Union's Strategic Energy Technology (SET) Plan. It was established in 2008 by leading research institutes to expand and optimise EU energy research capabilities. Today it brings together more than 250 organisations from 30 countries.
18 Joint Programmes
www.eera-set.eu

## Slide 5: EERA Joint Programme on Energy Storage
www.eera-energystorage.eu
NUMBERS and FIGURES
Launch: 2011
Members: 40 RTOs
and universities
Countries involved: 15
Energy storage areas: 5
MAIN ACTIVITIES
Mobility Scheme
Online PhD Days
JP ES Award
Policy and Technical Workshops
White Papers
Technology Roadmaps
Industry Advisory Board
Coordinator:
Dr. Myriam E. Gil Bardají
VISION
Accelerating the European energy storage research to achieve a renewable-based carbon neutral Europa by 2050.
https://www.eera-energystorage.eu/

## Slide 6: 2050 Storage Demand
2

## Slide 7
Renewables in Europe

## Slide 8: Why energy storage is needed? Long-term energy storage demand for energy independence
Source:
1 https://yearbook.enerdata.net/total-energy/world-consumption-statistics.html
2 https://download.terna.it/terna/1-DATI%20GENERALI_8d9cece053250fa.pdf
3 https://op.europa.eu/en/publication-detail/-/publication/94aab140-8378-11ea-bf12-01aa75ed71a1/language-en
1266 TWh long-term energy storage capacity need
Assumptions:
21399.2 TWh European primary energy consumption (2018)
Elaboration over 2015-2020 generation data (ENTSO-E)
36% Energy Storage cycle efficiency
5.8% POWER GRID LOSSES
Chart: 
| January | February | March | April | May | June | July | August | September | October | November | December
expected generation (TWh) | 1646.1004 | 1739.0841 | 2091.6909 | 2042.7722 | 2156.0407 | 2068.4508 | 2167.1172 | 2037.3065 | 1856.8686 | 1634.4907 | 1499.4516 | 1656.0404
surplus/lack with respect to the annual mean (TWh) | -236.8507 | -143.867 | 208.7397 | 159.821 | 273.0895 | 185.4996 | 284.166 | 154.3553 | -26.0826 | -248.4605 | -383.4996 | -226.9108
 |  | NORTH | CENTRE | SOUTH
45% 3 | PV | 0,3 | 0,15 | 0,55
45% 3 | wind | 0,65 | 0,05 | 0,3
Total generation vs surplus/lack (TWh)
Generation profiles (TWh)

## Slide 9: Green Deal Policy Specification
A generation of 2250 TWh is needed for ~50 M tons hydrogen
112 TWh are needed for buffering the electric grid
Hydrogen storage will key for the society.
For how long ? One month ? => (50/12) ~ 4.2 M tons H2
In the ambious scenarios hydrogen will be a key vector
for the society and the industry
Hydrogen demand in TWh
generation power in 2050
under various scenarios
There is no issue with seasonal power buffering,
if we can store hydrogen in sufficient amounts.
Notes: Across sectors, we see the potential for generating approximately 2,250 terawatt hours (TWh) of hydrogen in Europe in 2050, representing roughly
a quarter of the EU’s total energy demand . This amount would fuel about 42 million large cars, 1.7 million trucks, approximately a quarter of a million buses, and more than 5,500 trains. It would heat more than the equivalent of 52 million households
(about 465 TWh) and provide as much as 10% of building power demand. In industry, approximately 160 TWh of
hydrogen would produce high-grade heat and another 140 TWh would replace coal in steelmaking processes
in the form of direct reduced iron (DRI). 120 TWh of hydrogen combined with captured carbon or carbon
from biomass would also produce synthetic feedstock for 40 Mt of chemicals in 2050.

## Slide 10: Energy Storage
Today’s flexibility requirements – in 2021, 11% of the total electricity demand in EU
– will grow to 24% in 2030 and to 30% in 2050.
This translate into
(500 / 6)
~ 83 TWh/month
in winter period
And ~ 250 TWh
for 3 month
seasonal storage

## Slide 11
Cost of Green Hydrogen Production Deployment
IRENA report: Green Hydrogen Cost Reduction 2020
1.5 – 3.5 $ / kg H2
in 2030

## Slide 12
Effective costs of a conventional hydrogen storage system*
Low : 0.2 €/ kg (salt cavern) 1.8 €/kg (gas field) high: 4.5 €/kg (LOHC)
* DIHK Faktenpapier Juni 2020
Costs for standard hydrogen production plus storage
results in 1.7 – 8 € /kg hydrogen.
Reference Scenario : Costs for Hydrogen Stored in 2030
PEM electrolysers still need critical raw materials (iridium, platinium, etc)
and PFAS. The avoidance may reduce the efficiency and generate higher cost.
In economy terms alkaline water electrolysis is seen to be worse,
but could be easier to scale up.
Issue to scale up: Today ~140 MW electrolysers are operational.
Repower EU target is 140 GW !
Notes: In 2021, water electrolysis accounted for only around 0.1% of global hydrogen production.

## Slide 13: Reactive Metals as Energy Storage Medium
3

## Slide 14: Short Discussion on Long-term Storage Media
Fe : Complex reduction process, still premature.
Ammonia : Needs cooling, that will drop efficiencies for seasonal application. Main use as fertilizer!
Flow batteries: Vanadium is a rare material and the energy density is extremly low (10-20 Wh/kg).
Pumped hydro : Capacity is limited 220 GWh in Europe (Set-Plan); Society might have objections!
Bio materials: Have capacities of about 1000 TWh.
Liquid air energy storage: Good for daily storage.
Hydrogen: Critical raw materials, PFAS, scale up for now,
Large scale storage and use of hydrogen is not proven, yet
Aluminium: May be .. , reduction process is available in industrial scale!
To be discussed.

## Slide 15: How can We Replace Materials from Non-Energy Consumption ?
4 PJ ~ 3.6 PJ = 1 TWh

## Slide 16: Biomass
100000 toe ~ 1 TWh
Non-energy consumption by fuel (ca. 1000 TWh) could be covered by bio-mass in the future.
Taken from the „National renewable action plan“ (NREAP)

## Slide 17: Potential Hybrid Energy System
Could be combined with a geothermal
heat source reducing the loses and
costs
Seasonal storage should have
long term high efficiencies

## Slide 18
Reactive metals (and Al) vs. Energy Storage Needs
Total energy: 1200 TWh
Total energy: 29 TWh
Barelli, L.; et al.. Reactive Metals as Energy Storage and Carrier Media: Use of Aluminum for Power Generation in Fuel Cell-Based Power Energy technology, 8 (9), Art. Nr.: 2000233. doi:10.1002/ente.202000233
in Orientation to Taylor, Peter; et al.l (2012). Pathways for Energy Storage in the UK. Centre for Low Carbon Futures, York.
Baumann, M.; et al. A review of multi-criteria decision making approaches for evaluating energy storage systems for grid applications. 2019. Renewable & sustainable energy reviews, 107, 516–534. doi:10.1016/j.rser.2019.02.016

## Slide 19: Energy carriers for long-term energy storage Reactive metals (e.g., aluminium) enable easy, low cost, “perennial” storage
P. Julien, J. M. Bergthorson, Sustainable Energy Fuels (2017) 1, 615.
D. J. Durbin and C. Malardier-Jugroot, Int. J. Hydrogen Energy (2013) 38, 14595–14617.
Al | Reactive metals
 | Constraint #1 : High reactivity Competitive energy density
 | Constraint #2 : No critical material
 | Constraint #3 : CO2 emission free reduction
 | Constraint #4 : No toxicity or hazard risk No PFAS
 | Constraint #5 : Local availability & Transportability
 | Constraint #6 : Recyclability
Chart: Gravimetric Energy Density [kWh/kg]
| 12.8889 | 14.8889 | 14.8889 | 14.8889 | 12.666700000000001
Conventional | 9.5 | 6.1667 | 0.01001 | 2.5 | 10.7222
Other | 0.0033 | 1.4786 | 2.79 | 1 | 0.73056 | 3.1945
Metals | 40.8446 | 34.1922 | 24.6672 | 23.3065 | 16.1192 | 12.6302 | 10.638 | 6.8333 | 6.8059 | 22.4436 | 5.4
Notes: Li batteries : 0.3 kWh/kg // Fe :

## Slide 20: Aluminium as Driver of a Circular Storage System for Hydrogen, Power and Heat
Barelli, L.; et al..
Al2O3 reduction to Al through carbon-free Hall-Héroult process
Wet combustion
2Al(s)+3 H2O(g) Al2O3(s)+3H2 (g) -815.4 kJ/mol
Thermodynamic conversion
H. Ersoy, M. Baumann, L. Barelli, A. Ottaviano, L. Trombetti, M. Weil, S. Passerini, Adv. Mater. Technol. 2022, 7, 2101400.
1 kg of Al produces:
4.2 kWh heat
0.11 kg H2
1.9 kg Al2O3 (to be recycled in the Al production)
circular approach
recyclable energy carrier

## Slide 21
Carbon Free Hall-Héroult Process
Zero CO2 emission, only O2
No perfluorochemicals (PFCs) emitted
20 % less energy and flexible power
50 % less space, see figures
40 % less investments
15-30 % less operational costs
Presentation by: Eng. Jon Hjaltalin Magnusson, M.Sc.EE., CEO
Arctus Aluminium Ltd., Reykjavik, Iceland // jhm@arctus.is
The capacity of the new
electrolyser is about
1 tonne of aluminium
per day at a current
of 140,000 A.
Notes: PFCs are produced when fluorine from a salt used in electrolysis combines with the carbon in the anodes. The PFCs produced during electrolysis are extremely potent greenhouse gases, with a global warming potential of 6,500 and 9,200 times the strength of CO2, respectively. In 2021, Century Aluminum’s Sebree plant in Kentucky emitted 24 tons of PFCs, equivalent to the emissions of 40,000 cars.
Inert anodes may reduce local air pollution. In addition to the climate benefits that they offer, inert anodes also present an opportunity to decrease sulfur dioxide (SO2) pollution. Carbon anodes are produced by baking coke and coal tar pitch, which both contain sulfur. SO2 is produced during smelting when oxygen in the air reacts with sulfur in the carbon anodes. This reaction does not occur when using inert anodes, removing SO2
emissions from the smelting process.
Despite the climate and health benefits of inert anodes, one criticism of the technology is its potential impact on the electrical grid. The theoretical minimum electricity requirement for smelting with a carbon anode is 5.99kWh/kg Al, while for inert anodes, it is 9.03 kWh/kg Al. The higher theoretical energy usage is valid reason for concern about grid reliability and the ability to meet demand. This concern is especially relevant as policymakers work to decarbonize the electrical grid while simultaneously electrifying sectors like transportation and buildings.
However, there is research suggesting that the actual, nontheoretical energy requirements for inert anodes will be equal to or lower than traditional aluminum production processes. Use of inert anodes allows for a lower anode overvoltage (the extra energy needed to force a reaction), which ultimately reduces energy demand during electrolysis. Additionally, the distances between the anode and cathode can be reduced when inert anodes are combined with wetted cathodes, which can lower the energy requirement of the smelting reaction.

## Slide 22
Carbon Free Hall-Héroult Process - Products
Products:
Production cells with vertical inert
metallic anodes, ceramic cathodes
and control systems for aluminium
production.
The business and market potential has
estimated sales in 2030-2040 in Europe
of process cells, etc. for conversion of
8 old smelters: Estimated total revenues
in the period 2030 –2040: €4,5 billion.
Overall 19 smelters are operational in Europe.
99.7 % pure aluminium
Notes: PFCs are produced when fluorine from a salt used in electrolysis combines with the carbon in the anodes. The PFCs produced during electrolysis are extremely potent greenhouse gases, with a global warming potential of 6,500 and 9,200 times the strength of CO2, respectively. In 2021, Century Aluminum’s Sebree plant in Kentucky emitted 24 tons of PFCs, equivalent to the emissions of 40,000 cars.
Inert anodes may reduce local air pollution. In addition to the climate benefits that they offer, inert anodes also present an opportunity to decrease sulfur dioxide (SO2) pollution. Carbon anodes are produced by baking coke and coal tar pitch, which both contain sulfur. SO2 is produced during smelting when oxygen in the air reacts with sulfur in the carbon anodes. This reaction does not occur when using inert anodes, removing SO2
emissions from the smelting process.
Despite the climate and health benefits of inert anodes, one criticism of the technology is its potential impact on the electrical grid. The theoretical minimum electricity requirement for smelting with a carbon anode is 5.99kWh/kg Al, while for inert anodes, it is 9.03 kWh/kg Al. The higher theoretical energy usage is valid reason for concern about grid reliability and the ability to meet demand. This concern is especially relevant as policymakers work to decarbonize the electrical grid while simultaneously electrifying sectors like transportation and buildings.
However, there is research suggesting that the actual, nontheoretical energy requirements for inert anodes will be equal to or lower than traditional aluminum production processes. Use of inert anodes allows for a lower anode overvoltage (the extra energy needed to force a reaction), which ultimately reduces energy demand during electrolysis. Additionally, the distances between the anode and cathode can be reduced when inert anodes are combined with wetted cathodes, which can lower the energy requirement of the smelting reaction.

## Slide 23: Aluminium Combustion Technology
Steam
Fluidized bed
THERMODYNAMIC CONVERSION
(wet combustion)
Stored energy is converted into H2 and heat
Heat is transformed into electricity via gas turbine.
Is a simple combustion process !
Al powder
Al2O3
Overheated steam
Hydrogen
H2 bubble

## Slide 24: Hydrogen Storage Media Performance
Aluminium

## Slide 25: Business Case: Power Only
Barelli, L.; et al..
Al2O3 reduction to Al through carbon-free Hall-Héroult process
H. Ersoy, M. Baumann, L. Barelli, A. Ottaviano, L. Trombetti, M. Weil, S. Passerini, Adv. Mater. Technol. 2022, 7, 2101400.
Hydrogen is converted into power via a Solid Oxide Fuel Cell !

## Slide 26
Energy Carrier | Conversion Technology | Round Trip Efficiency (RTE) | Energy Density [kWh/L]
Al | Aluminium Wet – Combustion (ST,GT, & SOFC) | 35.6 % | 23.5
H2 | PEM Electrolyzer – PEM Fuel Cell (PEMFC) Reversible – Solid Oxide Cell | 30% (H2@200 bar) 48% (H2@70 bar) | 0.53 0.2
Methanol / DME | Solid Oxide Electrolizer (SOE) / H2 to methanol-DME / Solid Oxide Fuel Cell (SOFC) | 36% (26.5%) | 5.5
Gasoline | SOE/ H2 to gasoline/SOFC | 27% (20%) | 8.8
LNG | SOE/TSA dehydration, H2 and CO2 membrane separation/SOFC | 28% (23%) | 5.8
Volumetric energy density and implemented technologies of
Power-to-Power applications based on different energy carriers
The RTE values in brackets include the thermal (1750 kWh/tCO2) and electric (250 kWh/tCO2) specific consumptions for CO2 direct air capture for low-temperature solid sorbent technologies
Round Trip Efficiency

## Slide 27: REVEAL Project
at ~280 degrees C
Results are excellent
Batch operating system
Not suitable for continuous operation of energy-conversion devices such as turbines and fuel cells.
Energy density is lower than by producing alumina

## Slide 28: Storage System Cost
4

## Slide 29: European View on an Aluminium Storage System
43 M tons of aluminum is needed to store the power for 112 TWh.
Scale up of the European aluminium smelter industry by a factor of three to six
over 25 years would do it.
And Europe needs an increase of 22% „fresh“ aluminium production.
43 M tons aluminium would provide 4,7 M tons hydrogen storage.
This is a reserve for 34 days.
Aluminium production in 2022 :
World total : 69 M tons
Europe : 7 M tons
Aluminum is the third most
abundant element in the
earth's crust!
Aluminium demand in Europe :
2022 : 9 M tons
2050 : 18 M tons expected

## Slide 30
Today generation of hydrogen by wet combustion results in price of 12 -14 €/ kg
Inert aluminium smelting technology will reduce the price to 8-10 €/ kg of hydrogen.
Aluminium is a hybrid storage medium. There is still heat and power left.
Seasonal storage will be actived, when power is rare and the price of electricity is high.
Revenues will reduce the hydrogen price further to may be 5-9 €/ kg.
The March 2010 commodity price for aluminum is $2.21 per kg. Al2O3 At this price, hydrogen from an aluminum-water hydrogen generation approach would cost approximately $20 per kg H2. Even assuming high volume production, the DOE target range for hydrogen cost of $2-3 per kg H2 would not be met.
Private Cost Assessment

## Slide 31: Aluminium Redox Cycle vs Pressurized Hydrogen
https://www.sciencedirect.com/science/article/pii/S2666352X22000413
Based on 280 C Aluminium wet combustion

## Slide 32
Cost calculations are based on todays market framework and are rough estimations.
Aluminum could be the medium for daily, weekly or seasonal storage solution.
Aluminium could be the medium for local or central energy solutions. Turbines from coal or gas power stations could still be used !
The ambitious scenario of the EU assumes an overall energy drop by a factor of 1.5 – 2
EU Green Deal scenario is most likely are not realistic.
If the energy consumptions is not dropping and Europe still needs 1200TWh seasonal storage capacities in 2050, then this is a challenge.
Aluminium production from bauxite has an environmental issue. Using aluminium in a circular economy is a clean process.
Remarks

## Slide 33: StoRIES project H2020 project
5

## Slide 34: Storage Research Infrastructure Eco-System
34
MAIN OBJECTIVES
Foster a European eco-system of industry and research organisations on hybrid energy storage technologies
Provide access to world-class materials and energy storage related research infrastructures
NUMBERS and FIGURES
Duration: 2021-2025
Budget: 7 Mio €
Beneficiaries: 47
Infrastructures: 64
Countries involved: 17
Key Research Priority: Hybridization of ES
ECO-SYSTEM
Coordinator:
Prof. Stefano Passerini
This project has received funding from the European Union’s Horizon 2020 research and innovation program under Grant Agreement no. 101036910

## Slide 35: Main Outcomes
White Paper on ‘Open Data in the ES community’
6 Transnational Access (TNA) calls
Sustainable ES Workshop Series
White paper on ‘Sustainable hybrid ES for the European CET’
Materials Acceleration Platform for ES (MAPs)
Roadmap for Hybrid Energy Storage Solutions
Strategic Research and Innovation Agenda (SRIA)
5 International Mobility Calls
Master programme
Mentoring Programme
3 Summer schools
This project has received funding from the European Union’s Horizon 2020 research and innovation program under Grant Agreement no. 101036910
www.storiesproject.eu

## Slide 36
eera-jpes@b3.kit.edu
EERA JP-ES Energy Storage
@EERA_JPES
eera-energystorage.eu
Thank You Very Much For Your Attention
Many Thanks for Supporting this Presentation
Stefano Passerini
Project coordinator
Myriam Gil Bardají
EERA Joint Programme coordinator
Linda Barelli
University of Perugia

## Slide 37
Some Extra Slides

## Slide 38: Primary and Alumina Production Facilities
Alumina
Primary

## Slide 40: Work on inert anodes – at SINTEF and globally
There are currently many research groups working on inert anodes.
The Russian company RUSAL is currently operating with pilot cells based
on the use of metal anodes. A Chinese company has pilot cells using
cermet anodes (made of a mixture of a metal and ceramic material).
Elysis is a relatively new consortium made up of the companies Alcoa,
Rio Tinto, Apple and the Canadian authorities. Elysis is planning to
spend more than a billion kroner on the development of cell technology
based on the use of inert anodes, and are claiming that they will have
a commercial process in place in 2024.
In Europe, Arctus Metals in Iceland is conducting R&D into inert anodes.

## Slide 41
industrial production of primary aluminium in Hall-Héroult electrolysis cells, where alumina (Al2O3) is dissolved in a molten fluoride-containing electrolyte consisting mainly of cryolite (Na3AlF6) at about 960 °C.