## Slide 1: Analysis of the electric energy storage in different renewable energy scenarios
Wayne Götz, Tobias Tröndle, Ulrich Platt und Werner Aeschbach-Hertig
University of Heidelberg
DPG Frühjahrstagung – Dresden | 4. März 2013

## Slide 2: Global Energy Supply Model
Input:
energy production mix
overcapacity
load management
electromobility
Output:
timeseries
storage capacity
installed capacity of energy production
…
Restrictions:
resolution of area: 2.5° (MERRA)
resolution of time: 1h
perfect electricity grid
storage efficiency: 81%
demand curve (Germany 2008)
10 types of energy producers
MEET*
*Meteorological based Energy Equilibrium Testing
Notes: Kurze Vorstellung was das Modell kann

## Slide 3: demand in Europe analysis of frequencies
365 (24h)
≈ 1 week
Database: 2010_mix
demand
demand
FFT demand
frequency [year-1]
= 1 year
|Y(f)|

## Slide 4
365 (24h)
≈ 1 week
Database: 2010_mix
photovoltaics in Europe analysis of frequencies
supply
supply
FFT PV
frequency [year-1]
= 1 year
|Y(f)|

## Slide 5
365 (24h)
≈ 2 weeks
Database: 2010_65on_35off
supply
supply
wind onshore in Europe analysis of frequencies
FFT wind onshore
frequency [year-1]
= 1 year
|Y(f)|

## Slide 6: renewables and their consequences on storages
need of energy storage for Europe*
% of installed renewables
storage capacity [TWh]
storage capacity
[% of annual electricity demand]
mix of energy
storage
[% of power demand]
best energy
mix for Europe
60% sun & 40% wind
influence of the energy mix
on storage
*Tröndle, T., Platt, U., Aeschbach-Hertig, W. and Pfeilsticker, K. (2012), Erneuerbare Energie für Europa.
Physik in unserer Zeit, 43: 300–306.
need of storage
increases
strongly
Notes: Ab einem best. Anteil an EE

## Slide 7: tranferscenarios
renewables
name wind onshore wind offshore photovoltaics wave power hydro power CSP power bio power nuclear power coal power gas power | 2010_mix45 20% 30% 5% 5% 5% 10% 10% 15% | 2010_mix35 26% 39% 5% 5% 5% 10% 15% | 2010_mix20 30% 45% 5% 5% 5% 10% | 2010_mix10 34% 51% 5% 5% 5%
20% controllable
35% controllable
10% controllable
45% controllable

## Slide 8: scenarios
renewables
name wind onshore wind offshore photovoltaics wave power hydro power CSP power bio power nuclear power coal power gas power | 2010_100sun 100% | 2010_65on_35off 65% 35% | 2010_60_40 40% 60%
0% controllable
0% controllable
0% controllable

## Slide 9: 2010_60_40 in Europe
Amount of total accumulated stored energy:
Storage: 8.29 ∙ 1011 kWh
Storage (>24h): 3.17 ∙ 1011 kWh
Storage (<24h): 7.72 ∙ 1011 kWh
storage
[% of power demand]
storage
[% of power demand]
FFT Storage
*Percentage of total energy consumption
max = 1.0 ∙ 1011
max = 3.4 ∙ 109
365 (24h)

## Slide 10: overview of installed storage capacity in different scenarios
Chart: influence of the energy mix on installed storage capacity
| mix45 | mix35 | mix20 | mix10 | 60_40 | 100sun | 65on_35off
max(storage) | 376154000 | 3798800000 | 12975000000 | 134480000000 | 104600000000 | 596760000000 | 357970000000
max(storage (>24h)) | 0 | 2444800000 | 10999000000 | 132200000000 | 101540000000 | 590940000000 | 356970000000
max(storage (<24h)) | 376154000 | 1463800000 | 2235200000 | 2657400000 | 3416000000 | 6767100000 | 1704800000
in the 2010_60_40 scenario the installed storage (>24h) capacity is ≈ 30 times higher than the installed storage (<24h) capacity

## Slide 11: overview of the quantity of cycles the storages are used
Chart: influence of the energy mix on quantity of cycles
| mix45 | mix35 | mix20 | mix10 | 60_40 | 100sun | 65on_35off
cycles(storage (>24h)) | 2.9246 | 6.537 | 2.1634 | 3.1219 | 1.0086 | 1.3054
cycles(storage (<24h)) | 15.7382 | 87.4436 | 157.0329 | 227.6661 | 225.9953 | 252.6932 | 98.5453
in a 100% renewable energy scenario the storage (>24h) is used only once a year and the
storage (<24h) is used up to ≈ 2/3 days a year

## Slide 12: storage technologies
storage technologies | energy density (kWh/m³)
Hydrogen | 3 (Atmospheric pressure); 530 (20 MPa); 1400 (70 MPa)
Compressed Air Storage | 3 (Δp =2 MPa); 12 (Δp =8.5 MPa)
Pumped-storage Hydeoelectricity | 0.82 (300m drop height)
overview storage capacity of different energy storage systems*
*Energy [R]evolution, Greenpeace, June 2012, 259
1h
24h
1m
1a
discharge time [h]

## Slide 13: summary and outlook
summary
installed long-term storage (>24h) capacity can be around 30 times higher than short-term installed storage (<24h) capacity
short-term storage will be used up to 2/3 days and the long-term storage from 1 to 3 times a year
outlook
analysis and optimization of the separation of storage in short-term and long-term
analysis of the transfer process into a 100% renewable scenario
analysis of the variation of storage from 2000 – 2010

## Slide 14
thank you very much
for
your attention