## Slide 1: Nuclear fusion on the way to ITER and beyond
Thomas Pütterich
and the ASDEX Upgrade Team
AUG laser scan

## Slide 2: Outline
Introduction to nuclear fusion with magnetic confinement
How does a tokamak fusion device work?
Critical open questions
  Future plans

## Slide 3: Nuclear fusion with D-T
Neutron
Deuterium
4Helium
Tritium
3.5 MeV
14.1 MeV
Tritium does not occur naturally.
It decays with a half time of 12.3y.
4Helium
6Lithium
4.8 MeV
0.015% Deuterium in sea water
Lithium will be provided in the breeding blanket around the vacuum chamber

## Slide 4: D-T fusion rate coefficients set temperature range
Source: Wikipedia
Ion temperature range: 10 - 30 keV
(100-300 Mio Kelvin)
Coulomb collisions orders of magnitude
more likely than fusion events  thermal plasma
Energy confinement time a few seconds:
density ~ 1020 m-3
allowing fusion alphas (1/5 of power)
to compensate energy loss

## Slide 5: Reactor Schematics for Magnetic Confinement Fusion
Graphic: IPP, Karin Hirl
No long-lived waste
No chain-reaction
Base load electricity
No CO2

## Slide 6: Two Lines of Experiment Types
Tokamaks (focus of this talk)
plasma current via transformer principle
Well developed concept => ITER
Stellarators
only external coils, no plasma current
one generation behind, but potentially the better solution for a reactor
central solenoid (transformer)
toroidal field coil
plasma current
magnetic field line
vertical field coil
toroidal field coil
helical field coil
coil current

## Slide 7: Magnetic container for charged particles
Magnetic field lines
flux surfaces
magnetic field lines
ASDEX Upgrade
const. pressure
(and T) on flux surfaces
Charged particles bound
to magnetic field lines
ASDEX Upgrade (video camera)

## Slide 8: Step-ladder of tokamak experiments
JET
6 m
80 m3
~ 16 MWth
(D-T)
ITER
12 m
800 m3
~ 500 MWth
(D-T)
diameter
plasma volume
fusion power
ASDEX Upgrade
3.3 m
14 m3
1.5 MW
(D-T equivalent)
Coil and divertor configuration very similar between ASDEX Upgrade and ITER & W as prominent wall material

## Slide 9: A view into the ASDEX Upgrade torus after 30 years of operation
first wall made from W since 2007

## Slide 10: Open problems in tokamak research
Power exhaust
Avoidance of transients (edge localised modes, disruptions)
Stationary tokamak operation
Predicting the plasma properties
Individual solutions for 1-4 available, but integration into 1 reactor scenario challenging

## Slide 11: Open problems in tokamak research
Power exhaust
Avoidance of transients (edge localised modes, disruptions)
Stationary tokamak operation
Predicting the plasma properties
Individual solutions for 1-4 available, but integration into 1 reactor scenario challenging

## Slide 12: Power balance in ITER
50 MW
500 MW
400 MW leave as neutrons
converted to heat in the blanket
100 MW heat plasma ( particles)
50 MW additional heating for control
150 MW have to be transmitted to cooling system:
50 MW core radiation, 100 MW to divertor
fusion amplification factor =10
Power exhaust can be developed and tested in smaller device ASDEX Upgrade:
power/radius good scaling parameter for similar edge plasma parameters:
divertor radiation

## Slide 13: Tungsten divertor erosion switched off with nitrogen seeding
W erosion switched off when Te < 4 eV
Note that a high plasma density is required
to for efficient divertor cooling

## Slide 14: Video: effect of nitrogen seeding on divertor heat load

## Slide 15: Power balance in a reactor: need to add outer core radiation
80 MW
2000 MW
1600 MW leave as neutrons
converted to heat in the blanket
400 MW heat plasma ( particles)
80 MW for control, current drive
480 MW have to be transmitted to cooling system:
360 MW core radiation, 120 MW to divertor
fusion amplification factor =25
similar to ITER solution ?
may be more challenging in a reactor due to lower divertor density
 alternative divertor ?
strong outer core radiation
combination of outer core and divertor radiation calls for an impurity mix (e.g., Ar + Xe)

## Slide 16: Open problems in tokamak research
Power exhaust
Avoidance of transients (edge localised modes, disruptions)
Stationary tokamak operation
Predicting the plasma properties
Individual solutions for 1-4 available, but integration into 1 reactor scenario challenging

## Slide 17: Transients: Avoid of Mitigate
Edge localized modes: repetitive power pulses, degrade W divertor surface
(Disruptions: Strong forces on plasma facing components, structural elements and coils)
 Video

## Slide 18: Suppression of edge localized modes (ELMs)
ELMs degrade tungsten surfaces in the divertor and may lead to excessive W erosion
After repetitive power loading with 20-25 MW/m2 in GLADIS
 a high number of large ELMs not tolerable in ITER / fusion reactor
23
~50 mm

## Slide 19: Steep edge transport barrier (ETB) root cause for ELMs
steep pressure profiles
Er gradients
edge current density peak j
p’ and j drive instabilities
magneto-hydrodynamic
ELMs = edge localised modes
Te
ne
<j>
Er
Te (keV)
ne (1019 m-3)
j (MA m-2)
Er (kV m-1)
10
8
6
4
2
0
E. Wolfrum et al. Nuclear Fusion 2015 and DPG, Munich, 2019
ETB sets boundary condition for core plasma performance and occurence of edge localized modes
ETB
-10
-20

## Slide 20: Suppression of edge localized modes (ELMs)
16 dedicated magnetic perturbation coils
installed in ASDEX Upgrade
Edge transport barrier ameliorated
ELMs completely suppressed
Note: works in ASDEX Upgrade
only at very low density
(relevant non-dimensional parameter
not yet identified. If low collisionality
required, fine for ITER)

## Slide 21: Open problems in tokamak research
Power exhaust
Avoidance of transients (edge localised modes, disruptions)
Stationary tokamak operation
Predicting the plasma properties
Individual solutions for 1-4 available, but integration into 1 reactor scenario challenging

## Slide 22: Route towards stationary operation
Loop voltage can be brought to zero
by NBI and ECRH current drive (NICD,ECCD) and
internal bootstrap current
Current profile shaping required to avoid
MHD instabilities
This corresponds to stationary tokamak operation
Note: low density is required to make
current drive efficient

## Slide 23: Open problems in tokamak research
Power exhaust
Avoidance of transients (edge localised modes, disruptions)
Stationary tokamak operation
Predicting the plasma properties
Individual solutions for 1-4 available, but integration into 1 reactor scenario challenging

## Slide 24: GENE code predicts turbulent transport in the plasma core
genecode.org
Quite well validated vs.
experiment
(with pedestal top as
boundary condition)
Turbulence driven by
Ti, Te
Influence of Te/Ti, rotation,
fast particles, impurities, ..

## Slide 25: Combination of reduced physics and empirical model for pedestal
ASDEX Upgrade energy confinement well decribed using engineering parameters
Next: implementation for different tokamaks, model improvement,  tokamak flight simulator

## Slide 26: Summary
Good progress achieved on several key areas:
energy confinement, power exhaust, ELM and disruption avoidance
But not simultaneously in a single discharge! Not one set of dimensionless parameters.
Accompanying first principle modelling required for extrapolation
Pedestal region still lacks coherent physics description (but expected to come)
Integration of all this requires a large device  ITER
Final model validation by testing ITER predictions in 2030s

## Slide 27: ITER site as of May 2021 (first plasma planned Dec 2025)
Photo:
ITER Organization /
EJF Riche

## Slide 28: What next ?
The milestone for nuclear fusion develoment is a burning plasma in ITER
- ITER operation to start in Dec 2025, D-T fusion in 2036
regarding plasma physics, the step from ITER to a tokamak demonstration plant DEMO is not a very big one
  A tokamak DEMO will be ~ 30 % larger than ITER (in linear scale)
  Tungsten is reference surface material, but components can be further improved: e.g. by W fibre-reinforced W composites
  DEMO to start operation in the 2050s
Possibly the stellarator line qualifies as a reactor candidate (=> Stellarator DEMO?)

## Slide 29: Thanks to: The ASDEX Upgrade team
Special thanks to the AUG technical staff
for excellent work in operation, maintenance
and extension